## Slide 1
USAFA ASTRO
2026 Fall
Lab #8
KestrelSAT Capstone
Agentic AI Workflow
Getting started with Coding Agents
ASTRO 331 – Space Systems Engineering
Notes: This brief expands the Method slide from the Lab 8 guidance: how to go from a lab folder to agent-written, cadet-verified code on KestrelSAT.

## Slide 2
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Prerequisites
2026 Fall
Complete before your first agent session:
GitHub account
One per cadet. Verify student status at education.github.com for free Copilot access.
GitHub Desktop
Install and sign in with your GitHub account (GitHub Desktop is proffered for this class, but other Git utilities are fine).
VS Code + PlatformIO
Already installed from earlier labs. Confirm a lab project still builds.
Coding agent account
Claude Pro, or a free option (Codex, Copilot Student). See Agent Tool Options.
KestrelSAT GCS
Installed, with KestrelSAT, USB cable, and XBee radio on hand for testing.
Astro 331 Lab #8
2
Notes: Complete before the first agent session. GitHub account and Desktop sign-in are the common blockers; GitHub Education verification can take a few days.

## Slide 3
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Method (Review)
2026 Fall
SPECIFY
Verifiable requirements
GENERATE
Agent proposes a design
IMPLEMENT
Trusted tool(s) make it real
ADJUDICATE
Engineer owns the call
ITERATE
The general workflow for agentic coding is:
1
Create repo for your project and push it to GitHub
2
Open a new session in Claude Code/ChatGPT Codex/other coding agent
3
Connect your repo to the session
4
Work with the agent to generate commits for your project
5
Adjudicate agent work and iterate!
Astro 331 Lab #8
3
Notes: Recap of slide 5 of the Lab 8 guidance. The loop is the mindset; the five steps are the mechanics. Every remaining slide maps to one of the five steps.

## Slide 4
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Git Basics (Review)
2026 Fall
Local repo
your laptop (Git)
push
fetch / pull
Remote repo
GitHub (origin)
Term
Meaning
GitHub Desktop
Repository (repo)
A project folder whose full history Git tracks
Add / Clone repository
Commit
A saved snapshot of changes, with a message
Commit to <branch>
Push
Send your commits to GitHub
Push origin
Fetch / Pull
Check for / download commits from GitHub
Fetch origin / Pull origin
Branch
A separate line of commits; main is the default
Current branch menu
Diff
Line-by-line changes: + added, − removed
Changes tab / History tab
Pull request (PR)
A request on GitHub to merge one branch into another, with review comments
Create Pull Request (opens GitHub)
A coding agent uses these same operations: it commits to its own branch and pushes to GitHub. You fetch that branch to test it.
Astro 331 Lab #8
4
Notes: Review only. Git runs on the laptop; GitHub hosts the shared copy. The agent uses the same operations: it commits to a branch and pushes to GitHub, and cadets fetch that branch to test it.

## Slide 5
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Chat LLM vs. Coding Agent
2026 Fall
Chat LLM (copy/paste)
Coding agent (e.g. Claude Code)
Sees your code
Only what you paste in
Reads the whole repo itself
Edits code
You copy, paste, and merge by hand
Edits files and commits them to a branch
Runs commands
No
Yes, in a cloud sandbox (search, scripts, compile)
Project rules
Re-explained in every chat
Written once in CLAUDE.md, read every session
Your role
Integrator and debugger
Specifier, reviewer, and tester
An agent does more work per prompt. Each prompt needs a clearer specification, and each result needs a closer review.
Astro 331 Lab #8
5
Notes: Most cadets have only used chat LLMs. The key shift: the agent works directly in the repo, so the cadet's job moves from integrating code to specifying and verifying it.

## Slide 6
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Agent Tool Options
2026 Fall
Tool
Where it runs
Free access
Context file
Claude Code on the web (this ppt’s example)
Cloud sandbox, working from your GitHub repo
No. Pro plan or higher
CLAUDE.md
OpenAI Codex
Your laptop (app, CLI, VS Code extension); cloud tasks on paid plans
Yes, with a ChatGPT Free account: small allowance, local tasks only
AGENTS.md
GitHub Copilot agent mode
VS Code on your laptop; cloud agent on GitHub
Yes, for verified students (Copilot Student), credit-limited
.github/ copilot- instructions.md
The five workflow steps are the same for every tool.
With a local agent, Steps 2–3 become “open the repo folder in VS Code.” The agent edits your working copy; you review and commit in GitHub Desktop.
Plans and limits change often. Check each tool’s current plan page.
Astro 331 Lab #8
6
Notes: Claude Code on the web is the worked example, but the workflow applies to any coding agent. Codex (local tasks) and GitHub Copilot (verified students) have free access with usage limits. Plans change often; check current plan pages before committing a team to one tool.

## Slide 7
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Example: Ground Command 10
2026 Fall
SPECIFY
STARTING POINT
Astro331_Lab7_Code. process_main_menu() already handles commands 0–9, 98, and 99.
REQUIREMENT
KestrelSAT shall respond to ground command 10 with one telemetry line containing battery voltage, state of charge, gyro Z, mag X, and mag Y, formatted for the GCS plotter.
V:3.912,SOC:84.2,gZ:0.12,mX:-21.40,mY:14.75
VERIFICATION
Demonstration: send 10 from the GCS over XBee. The reply arrives on one line and the GCS plots all five channels.
Astro 331 Lab #8
7
Notes: One small feature carried through every step. Command numbers 0-9, 98, 99 are already used in the Lab 7 code, so the example uses 10. The requirement is written to be verifiable before any code exists.

## Slide 8
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 1: Create & Push Repo
2026 Fall
SETUP
1
Download the course repo. Copy the contents of Astro331_Lab7_Code into a new folder.
2
GitHub Desktop: File › Add local repository › select the folder › create a repository.
3
Commit to main: “Initial copy of Lab 7 code.”
4
Publish repository to GitHub (keep it private).
5
Open the folder in VS Code and run PlatformIO Build once, before any changes.
KestrelSAT-Capstone/
├─ platformio.ini
├─ include/
│ ├─ definitions.h
│ └─ sd_functions.h
├─ src/
│ ├─ main.cpp
│ └─ sd_funcitons.cpp
├─ lib/INA238-master/
├─ .gitignore
└─ CLAUDE.md
← Step 1b
Lab folder at the repo root, so PlatformIO opens it directly.
Astro 331 Lab #8
8
Notes: Seed the repo with one lab folder at the root so PlatformIO opens it directly. Build once before any changes: a clean baseline means later build errors came from new code.

## Slide 9
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 1b: Add CLAUDE.md
2026 Fall
SETUP
# KestrelSAT Capstone (Team 3)
## About us
- New to Arduino and C++. Explain each
change in plain terms before coding.
- Prefer simple code over clever code.
## Hardware - SparkFun Thing Plus ESP32
PlatformIO env: esp32thing_plus
- XBee: HardwareSerial(2), 9600 baud
- ICM-20948 IMU, MAX17048 gauge (I2C)
- Pin map: include/definitions.h
## Conventions - Commands: process_main_menu()
- Telemetry: Name:value,Name:value\n
- Mirror every XBee message to Serial
## Rules - Never change pins without asking
- Add libraries only via lib_deps
- No blocking waits in loop()
- You can't test on hardware: list
what I must verify on KestrelSAT
Claude Code reads CLAUDE.md at the start of every session.
Include what a new teammate would need: hardware, where the pin map lives, conventions, rules.
Start with /init : the agent scans the repo and drafts the file. Then correct and add the hardware facts it can’t see.
Keep it short. Add a rule each time the agent repeats a mistake.
Codex: /init writes AGENTS.md.
Copilot: Generate Chat Instructions writes .github/copilot-instructions.md.
Astro 331 Lab #8
9
Notes: CLAUDE.md is the most effective single thing a team can do to improve agent output. It is plain Markdown committed to the repo root. The About us section tells the agent the team is new to Arduino, so it explains its changes and keeps code simple. Cadets can also ask in any prompt: explain this like I've only done three Arduino labs. Codex reads AGENTS.md the same way.

## Slide 10
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 2: Open a Session
2026 Fall
SETUP
Claude Code
cloud sandbox
GitHub repo
shared source
Your laptop
Desktop + PlatformIO
KestrelSAT
USB
The session can read and change your repo. It cannot reach your laptop, its USB ports, or KestrelSAT.
ONE-TIME SETUP
1
Go to claude.ai/code and sign in.
2
Claude Code requires a paid plan (Pro or higher). For free options, see Agent Tool Options.
3
Connect GitHub when prompted. Install the Claude GitHub App on your capstone repo only.
4
Accept the Default environment (Trusted network access).
Astro 331 Lab #8
10
Notes: Emphasize the architecture: the agent never touches the hardware. GitHub is the hand-off point between the cloud session and the cadet's laptop. Note: Claude Code is not included in the Free plan; at least one teammate needs Pro.

## Slide 11
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 3: Connect Repo
2026 Fall
SETUP
1
New session: select your capstone repo and the main branch.
2
The session clones the repo and loads CLAUDE.md.
3
Send an orientation prompt before asking for any change:
YOU
Read CLAUDE.md and src/main.cpp. Summarize how ground commands are handled and list the command numbers already in use. Don’t change any files.
AGENT
Commands arrive over XBee or USB Serial and are dispatched by a switch in process_main_menu(). Codes in use: 0–9, 98, 99. Case 1 prints the help menu. Replies go to XBee and are mirrored to Serial.
Check the summary against the code. If the agent misunderstands the code now, its changes will be wrong too.
Astro 331 Lab #8
11
Notes: The orientation prompt costs one message and tells you whether the agent understands the code. In this example it confirms command 10 is free. If the summary is wrong, fix CLAUDE.md before going further.

## Slide 12
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 4: Plan Before Code
2026 Fall
GENERATE
YOU
Add ground command 10 that replies with one telemetry line:
V:<volts>,SOC:<pct>,gZ:<dps>, mX:<uT>,mY:<uT>
Send it over XBee and mirror it to Serial. Add it to the help menu. Use the existing lipo and imu_sensor objects; no new libraries.
Don’t write code yet. Give me a plan: files and functions you’ll change, and any questions.
AGENT
Plan (src/main.cpp only):
1. Add prototype send_state_telemetry().
2. Add case 10 to process_main_menu().
3. New function: call getAGMT(), read voltage, SOC, gyrZ, magX, magY; send one line to Xbee and Serial.
4. Add “10 - State telemetry” to the case 1 menu.
Question: should gZ use the same units and sign as lab6_run_test()?
YOU
Plan approved. Match lab6_run_test(). Implement it and commit.
Check the plan for: expected files only · real library functions · questions answered by you, not guessed.
Astro 331 Lab #8
12
Notes: Asking for a plan first is cheap and catches wrong assumptions before code is written. Good plans name files, functions, and open questions. The cadet answers the questions; the agent should not guess.

## Slide 13
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 4: Review the Commit
2026 Fall
GENERATE
claude/ground-cmd-10 · src/main.cpp +17 −0
@@ process_main_menu(), case 1 @@
Xbee.print("9 - Stream RW speed\n");
+ Xbee.print("10 - State telemetry\n");
@@ process_main_menu() @@
case 9: stream_RWspeed(); break;
+ case 10:
+ send_state_telemetry();
+ break;
@@ new function @@
+void send_state_telemetry() {
+ imu_sensor.getAGMT();
+ String s = "V:" + String(lipo.getVoltage(), 3)
+ + ",SOC:" + String(lipo.getSOC(), 1)
+ + ",gZ:" + String(imu_sensor.gyrZ(), 2)
+ + ",mX:" + String(imu_sensor.magX(), 2)
+ + ",mY:" + String(imu_sensor.magY(), 2);
+ Xbee.println(s);
+ Serial.println(s);
+}
Green + lines were added; red − lines were removed.
Read every line. You will be asked to explain it.
Ask about anything unclear: “Why call getAGMT() first?”
Select Create PR in the session. The team reviews the PR before merging.
Astro 331 Lab #8
13
Notes: The agent pushes to a new claude/ branch, never directly to main. Walk through the diff line by line. Cadets must be able to explain every line they submit.

## Slide 14
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 4: Branches & PRs
2026 Fall
GENERATE
main
claude/ground-cmd-10
Initial copy
main
Add command 10
a1b2c3d
Fix zero gZ
e4f5a6b
Merge PR #3
main
PR #3: review, test, then merge
Branch
A separate line of commits. main is unchanged until the branch is merged.
Each session creates its own branch (claude/…) and pushes every commit there, including fixes.
GitHub Desktop’s Current branch menu switches your local copy between main and the agent’s branch.
Pull request (PR)
A request on GitHub to merge a branch into main. It shows the diff, the commits, and a comment thread.
1
Select Create PR in the session.
2
Teammates comment on specific lines.
3
Test the branch on KestrelSAT (Step 5).
4
Merge only after it passes.
Astro 331 Lab #8
14
Notes: The agent never commits to main. Each session gets its own branch, and every commit in that session, including fixes, goes there. The pull request is where the team reviews the change and where it gets merged after the hardware test passes.

## Slide 15
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 5: Test on Hardware
2026 Fall
IMPLEMENT
ADJUDICATE
1
GitHub Desktop: Fetch origin, then switch Current branch to claude/ground-cmd-10.
2
PlatformIO: Build, then Upload to KestrelSAT over USB.
3
KestrelSAT GCS: connect to the XBee port, send 10, open the plot window.
PASS CRITERIA (FROM THE REQUIREMENT)
One line per command, with all five values: V:3.912,SOC:84.2,gZ:0.12,mX:-21.40,mY:14.75
Values are plausible: V 3.0–4.2, SOC 0–100, gZ ≈ 0 at rest.
Rotate KestrelSAT: gZ, mX, and mY respond in the GCS plot.
Astro 331 Lab #8
15
Notes: This is the only step that tests the requirement. Compiler, PlatformIO upload, and the GCS are the trusted tools. Until KestrelSAT confirms the behavior, the agent's commit is a proposal.

## Slide 16
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Step 5: Iterate & Merge
2026 Fall
ADJUDICATE
ITERATE
If it fails
Report what you observed and paste the output.
YOU
On hardware, command 10 returns V and SOC correctly, but gZ, mX, and mY are always 0.00. Serial output below. Find the cause and explain it before changing code.
[paste Serial output]
The agent pushes a new commit to the same branch. Fetch, build, upload, retest.
If it passes
1
Merge the PR on GitHub.
2
GitHub Desktop: switch to main, Pull origin.
3
Start a new session for the next requirement.
4
Add a rule to CLAUDE.md for any mistake the agent made twice.
Astro 331 Lab #8
16
Notes: Failure reports should contain observations and logs, not just 'it doesn't work'. One requirement per session keeps context small and commits easy to review.

## Slide 17
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Common Failure Modes
2026 Fall
Failure
KestrelSAT example
How you catch it
Invented function
imu_sensor.getGyroZ() (the library provides gyrZ())
Build error; check the library header
Invented library
lib_deps entry that isn’t in the PlatformIO registry
Search it in PlatformIO Libraries
Pin conflict
New sensor on pin 14, already ENCODER_PIN_A
Compare against definitions.h
Blocking code
while (!Xbee.available()) inside loop()
Heartbeat stops in the GCS
Scope creep
Unrequested “cleanup” of other functions
Diff touches lines you didn’t expect
Unverified claim
“Tested and working”
The agent can’t reach KestrelSAT; you test
Astro 331 Lab #8
17
Notes: Every row here has happened with embedded code. Agents produce plausible code that may reference functions or libraries that do not exist. The build, the pin map, and the hardware are the checks.

## Slide 18
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Documenting GenAI Use
2026 Fall
“This use of GenAI must be clearly documented as instructed, specifying how GenAI contributed and what the cadet did to revise or evaluate that content.”
GenAI Level 4, Lab 8 Guidance
Keep an AI_LOG.md in the repo, with one entry per session:
## 2026-10-14 · Ground command 10 Session: claude.ai/code link
Driver: Cadet A Reviewers: Cadets B, C
Prompts: orientation, plan, implement, fix zero gZ
Agent made: commits a1b2c3d, e4f5a6b (PR #3)
We changed: gZ convention (matched lab6_run_test)
Verified: GCS plot of all 5 channels, rotation test
Issue found: gZ, mX, mY read 0.00 on first upload
The commit history and PR discussion are also part of the record.
Astro 331 Lab #8
18
Notes: Level 4 requires documenting how GenAI contributed and what cadets did to evaluate it. An AI_LOG.md in the repo, one entry per session, meets that requirement and becomes part of the graded repo.

## Slide 19
Overview
Example
1 Repo
2 Session
3 Connect
4 Commits
5 Adjudicate
Pitfalls
GenAI Docs
Teams
Working as a Team
2026 Fall
An agent session belongs to one account, and teammates can’t join it. The GitHub repo is the team’s shared workspace.
OPTION A
One driver
One teammate with agent access runs the sessions.
The others review plans and PRs, and test on hardware.
Rotate the driver for each requirement.
OPTION B
Parallel drivers
Each teammate runs sessions on their own requirement and branch. Tools can differ.
Merge through PRs.
Don’t have two sessions editing the same function.
Either way: add every teammate as a collaborator on the repo (Settings › Collaborators). Never share agent account login credentials.
Astro 331 Lab #8
19
Notes: A Claude Code session belongs to one account; teammates cannot join it live. The repo is where collaboration happens. Do not share Claude login credentials.